## Slide 1: STP Preliminary Design Review
Ro Atre, Abdul Osilan, Meerav Shah, Connor Stapf

## Slide 2: Scientific Mission
Measure structural stability of the rocket.
Measure vibrational stability of the rocket.
Analyze how the flex and vibrational forces change throughout the flight.
Determine applicability of rocket-propelled delivery of fragile items/components.
Flex Sensor
Vibration Sensor

## Slide 3: Payload Structure
Allows for additional or fewer platforms based on necessity.
With current setup, the structure mass is 79.31g.
All hardware is standardized metric-unit parts.
Slots for wire connections through platforms.

## Slide 4: Fabrication Plan
Combination of 3D Printing and purchased hardware
  Relatively quick and cheap part production
  Standard hardware is easily sourceable from stores or distributors
  PLA plastic provides stable, rigid platforms for electronics to be mounted
Electronic assembly to be completed on a platform-by-platform basis before being mounted onto the threaded rods of the main structure
  Allows for easier testing before final construction
  More platforms can be produced if more horizontal space is required

## Slide 5: Primary Sensor Choice
GPS: Ultimate GPS Module PA1616D - 99 channel w/10 Hz updates - MTK3333 Chipset
Product ID: 5186
Barometer: MPL3115A2 - I2C Barometric Pressure/Altitude/Temperature Sensor
Product ID: 1893
Multimeter: Adafruit INA260 High or Low Side Voltage, Current, Power Sensor
Product ID: 4226
Flex Sensor: Short Flex Sensor
Product ID: 1070

## Slide 6: Voltage Table
Component | Voltage
Microcontroller | 3.3V
GPS | 3.3V
Barometer | 2-3.6V
Multimeter | 3V or 5V
Flex Sensor | 3.3V or 5V
MicroSD Shield | 5V

## Slide 7: Preliminary Parts List
SENSORS
Microcontroller (TBD)
GPS ($19.95, 5.7g)
Barometer ($9.95, 1.2g)
Multimeter ($9.95, 2.0g)
Flex Sensor ($7.95, 0.27g)
MicroSD Shield ($7.50)
Vibration Sensor ($0.95, 0.3g)
OTHER
MicroSD Card ($11.50)
Buzzer ($1.95, 0.7g)
Battery ($2, 1.9g)
Battery Charger (~$7)
Electrical Components (TBD)
Perf Board ($5)
Structure (Cost TBD, 79.31g)
Mounting Hardware (TBD)

## Slide 8: Programming Language & Microcontroller
MICROCONTROLLER
Teensy 3.5 or 4.1
Powered by 9V Battery
Price range ~$25-35
42 I/O Points
Voltage Regulator Onboard
3 I2C, SPI, CAN and 8 Serial Ports.
Team will decide exact microcontroller
PROGRAMMING LANGUAGE
Arduino
Cross Platform Compatibility
Convenient & Simple to fix
Help available if needed
Tons of libraries, C++ derivative, Active Community
Fits the scale of the project
Team has decided on this language

## Slide 9: Systems Block Diagram

## Slide 10: Cost & Mass Estimates
Components | Cost
All sensors except microcontroller | $71.65
Most non-sensor electrical, controller and structural components | $49.50
Remaining in case of unexpected expenses | $28.85
COST
Components | Mass
All sensors except microcontroller | 10.01g
Most non-sensor electrical, controller and structural components | 71.31g
Included for additional tolerance/error mass | 18.68g
MASS

## Slide 11: Con Ops